## Slide 1: Communication and Control Software Development for Experimental Unmanned Aerial System - Selected Issues
Dariusz Rzońca, Sławomir Samolej, Dariusz Nowak, and Tomasz Rogalski

## Slide 2: Agenda
UAV as Distributed Real-Time Control System
  Main Components
  Network Architecture
  Software Components
  Hardware Components
  Research Motivation
Stanag 4586 communication standard
Stanag 4586 implementation issues
Rapid prototyping of control system
  Control algorithm structure
  Testbed and automatic code generation
Summary and future research

## Slide 3: UAV as Distributed Real-Time Control System - Main Components
MP-02 Czajka ultra light aeroplane with:
Mechanical modifications
Build into actuators and sensors
On-board experimental autopilot, attitude and heading reference system (AHRS)
CAN and Ethernet networks
Radiomodem
Tarpan Honker truck with:
Computer Cluster
Radiomodem
Spare Power Supply

## Slide 4: UAV as Distributed Real-Time Control System - Network Architecture

## Slide 5: UAV as Distributed Real-Time Control System - Software Components

## Slide 6: UAV as Distributed Real-Time Control System - Hardware Components
Ground Station Cluster
Autopilot
Autopilot/ AHRS

## Slide 7: UAV as Distributed Real-Time Control System - Research Motivation
A new data-intensive network nodes has been incorporated into the system.
A new radio link is going to be introduced into the system.
Different UAS modules may be provided by separate providers.
Autopilot control algorithm is intensively modified.

## Slide 8: Stanag 4586 communication standard
Published by NATO
UDP based
Standard set of messages for inter GCS-UAV communication.
Makes it possible to separate GCS provider from UAV provider
802.3 network is applied as 1st and 2nd ISO/OSI layer

## Slide 9: Stanag 4586 implementation issues
#define MAKE_SET_MSB_FROM(x) \
void set_msb_from_##x(void * where, stanag_##x value) \
{ \
stanag_set_msb(where, value, stanag_##x##_size); \
}
Byte order must be preserved.
Untypical data types (Integer 3, Unsigned 5)
C language limitations

## Slide 10: Rapid prototyping of control system - Control algorithm structure

## Slide 11: Rapid prototyping of control system - Testbed and automatic code generation

## Slide 12: Summary and future research
12
12
New media and communication standards (from control engineering point of view) have been incorporated into the distributed real-time control system.
The way of software communication layer implementation for the system has been discussed.
The integration of different of hardware/software units to create a complete on-ground flight control system rapid prototyping testbed has been presented.
The final control system has been tested during on-flight tests.
Automatic take-of and landing (ATL) and automatic on-airfield navigation (AN) are as well as a new ground station software are on development stage.

## Slide 13: Thank You for Your Attention
13
13